## Slide 1
01
QECA PARAMETER-RESPONSE V&V
Verification deck for
parameter-response falsification
The deck assumes you do not want to line-by-line audit every implementation detail. Instead, you audit each structure and each interface by sweeping the knobs that should expose incorrect behavior first.
Report Order
Four structures: parameters and expected response
Six pairwise interfaces: direct or mediated
Expected behavior versus actual behavior slot
End with a repeatable execution checklist
Core matrix views in this study: reduced Ydm,in(ω), full Y(ω), Z→Y reductions, and readout-branch S21 with vector fitting.
Use this as the report front section before presenting any actual sweep results.

## Slide 2
02
Method
Three-Part Verification Logic
This deck is intentionally about verification first, solution verification second, and validation third.
1. Verification
Did the code implement the intended mathematical structure? Use parameter-response checks and decoupling limits.
2. Solution Verification
Are discretization, sweep resolution, matching windows, and fitting settings converged enough for this claim?
3. Validation
Do the trends and magnitudes still look like plausible physics, not only plausible numerics?
Operational Rule For This Study
Start with self-structure sweeps where the expected trend is simplest and strongest.
Move to direct interfaces and check monotonicity under the explicit coupling knob.
Treat the remaining three pairs as mediated only, and audit them with path-breaking null tests.
The report should make it obvious what would have broken first if the implementation were wrong.

## Slide 3
03
Topology
Model Topology Used By The Audit
This summary matters because some interfaces are direct in the netlist, while others are only mediated through an intermediate path.
A good verification report should respect the actual topology of the study model, not only the physical story we tell around it.

## Slide 4
04
Inventory
Pairwise Audit Inventory
Direct interfaces get sweep-based checks. Mediated interfaces get null checks and path-breaking checks.
This slide is the transition point between subsystem pages and pairwise-interface pages.

## Slide 5
05
Subsystem
Qubit
Treat the qubit as the reference oscillator. This is where monotonicity checks should be easiest and where nonphysical loss should be easiest to spot.
Knobs In This Study
l_q_h
c_q_f
c_g1_f, c_g2_f
qubit_port_res_ohm
Primary Matrix View
Primary observable: reduced Ydm,in(ω), extracted fq from Im(Ydm,in)=0, and Re(Ydm,in) at resonance.
Expected Qualitative Response
Lq up should move fq down.
Cq or pad-to-ground capacitance up should move fq down.
With c_xy = c_rq = 0, Re(Ydm,in) should stay small and smooth.
Pad asymmetry should affect CM/DM weighting, not spawn unrelated resonances.
What Counts As A Good Sign
Zero crossing moves monotonically under parameter sweeps.
Retuning the bare qubit does not suddenly create large loss.
Frequency extraction is stable under sweep refinement.
Actual behavior / plot slot
Insert: Lq sweep, Im(Ydm,in) zero-crossing traces, and one isolated-qubit sanity plot.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
Front section: first explain the structure, then explain what the structure should do when its own knobs are swept.

## Slide 6
06
Subsystem
Readout Resonator
In this study the readout resonator is the quarter-wave resonator branch coupled into the readout line through the coupled window.
Knobs In This Study
qwr_length_m
common_l_per_m_h, common_c_per_m_f
common_r_per_m_ohm, common_g_per_m_s
qwr_target_dz_m
Primary Matrix View
Primary observable: readout-line S21, fitted resonator poles from vector fitting, and optional local Y before reduction.
Expected Qualitative Response
Longer electrical length should move the readout-resonator resonance lower.
Changing common RLGC should shift distributed resonances consistently, not arbitrarily.
If c_rq1 = c_rq2 = 0, retuning the resonator should not move the qubit result.
Mesh refinement should converge mode locations instead of reordering them.
What Counts As A Good Sign
The narrower fitted resonance tracks the readout resonator consistently.
Resonance motion follows electrical length intuition.
The resonator disappears from qubit behavior when the qubit interface is opened.
Actual behavior / plot slot
Insert: qwr length sweep on S21 and fitted resonance markers with c_rq toggled on/off.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
Front section: first explain the structure, then explain what the structure should do when its own knobs are swept.

## Slide 7
07
Subsystem
XY Line
Important modeling fact: in this study the XY lane is represented as a terminated XY node plus the qubit-to-XY coupling capacitors, not as a long distributed geometry block.
Knobs In This Study
c_xy1_f, c_xy2_f
xy_port_res_ohm
common RLGC only matters indirectly here
No independent XY length parameter in this model
Primary Matrix View
Primary observable: port-3 loading in the full Y(ω) and its effect on reduced Ydm,in(ω).
Expected Qualitative Response
Increasing c_xy should strengthen the XY-only loading contribution.
Setting c_xy1 = c_xy2 = 0 should collapse the XY contribution cleanly.
Changing xy_port_res_ohm should alter dissipative loading but should not create readout resonances.
Any claim about XY distributed standing-wave motion should be treated carefully because this model does not expose an XY length knob.
What Counts As A Good Sign
XY-only loss vanishes in the zero-coupling limit.
XY trends are monotonic with c_xy sweeps.
The study narrative stays aligned with what the model actually contains.
Actual behavior / plot slot
Insert: c_xy sweep, xy_port_res sweep, and one note explaining the XY node abstraction.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
Front section: first explain the structure, then explain what the structure should do when its own knobs are swept.

## Slide 8
08
Subsystem
Readout Line With Purcell Filter
This is the distributed branch from readout input to output, including left line, half-wave Purcell filter, right line, and terminations.
Knobs In This Study
left_readout_length_m, right_readout_length_m
purcell_filter_length_m
pf_coupling_cap_in_f, pf_coupling_cap_out_f
readout_port_res_ohm
left/right/pf target_dz_m
Primary Matrix View
Primary observable: raw readout-line S21, fitted S21 model, and extracted Purcell-filter / readout-resonator resonances.
Expected Qualitative Response
Increasing electrical length should move the associated resonances or notches lower.
Changing PF coupling capacitors should alter bandwidth and feature strength.
Port termination changes should alter line response smoothly, not invent extra physics.
Discretization refinement should stabilize S21 features and fitted poles.
What Counts As A Good Sign
The broader fitted feature tracks the Purcell-filter mode consistently.
Mode motion is consistent with length scaling and coupling strength.
The branch can be characterized cleanly even when qubit couplings are disabled.
Actual behavior / plot slot
Insert: S21 sweeps versus PF length and coupling-cap sweeps, plus vector-fitting overlays.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
Front section: first explain the structure, then explain what the structure should do when its own knobs are swept.

## Slide 9
09
Interface
Qubit ↔ XY Line
Each pair should be audited by asking whether the parameter-response pattern matches the topology that this model actually contains.
Direct Interface
Controlling Knobs
c_xy1_f
c_xy2_f
xy_port_res_ohm
Primary Matrix View
Use reduced Ydm,in(ω) near qubit resonance plus selected full Y(ω) traces for port 3.
Expected Behavior
Increasing c_xy should increase XY-only loading and usually increase Re(Ydm,in).
c_xy imbalance changes the centroid weights w1 and w2, so asymmetry should show up systematically.
Setting c_xy1 = c_xy2 = 0 should collapse to the no-XY reference.
If This Fails, Suspect
Loss stays large even when c_xy is zero.
fq moves in the opposite direction with stronger XY loading without another explanation.
Random extra resonances appear when only c_xy is swept.
Actual behavior / plot slot
Insert: XY-only sweep panel with c_xy magnitude and imbalance variants.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
For mediated pairs, path-breaking null tests matter more than large parameter sweeps.

## Slide 10
10
Interface
Qubit ↔ Readout Resonator
Each pair should be audited by asking whether the parameter-response pattern matches the topology that this model actually contains.
Direct Interface
Controlling Knobs
c_rq1_f
c_rq2_f
qwr_length_m (alignment context)
Primary Matrix View
Use reduced Ydm,in(ω) at the qubit plus S21 context from the readout branch.
Expected Behavior
Increasing c_rq should strengthen readout-mediated frequency shift and loss.
Tuning the resonator closer to the qubit should increase loading.
Setting c_rq1 = c_rq2 = 0 should disconnect the qubit from the entire readout branch.
If This Fails, Suspect
The qubit still feels the readout branch when c_rq is zero.
Changing qwr length strongly affects the qubit with the interface opened.
Observed shift and loss move incoherently under the same c_rq sweep.
Actual behavior / plot slot
Insert: c_rq sweep, qwr detuning sweep, and readout-off null check.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
For mediated pairs, path-breaking null tests matter more than large parameter sweeps.

## Slide 11
11
Interface
Readout Resonator ↔ Readout Line + Purcell Filter
Each pair should be audited by asking whether the parameter-response pattern matches the topology that this model actually contains.
Direct Interface
Controlling Knobs
coupled_window_length_m
coupled_window_input_mode
q2d_* or modal even/odd parameters
pf_window_start_m, qwr_window_start_m
Primary Matrix View
Use raw S21, fitted S21 model, and extracted resonances from the readout branch.
Expected Behavior
Longer or stronger coupled-window interaction should increase hybridization.
Window length → 0 or mutual terms → 0 should decouple the resonator from the line.
Modal and q2d parameterizations should agree qualitatively on trend direction.
If This Fails, Suspect
The resonator feature does not respond to window strength at all.
The line still shows strong resonator loading with the window effectively off.
q2d and modal modes disagree on basic trend direction.
Actual behavior / plot slot
Insert: coupled-window length sweep, modal-vs-q2d comparison, and one decoupling limit plot.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
For mediated pairs, path-breaking null tests matter more than large parameter sweeps.

## Slide 12
12
Interface
Qubit ↔ Readout Line + Purcell Filter
Each pair should be audited by asking whether the parameter-response pattern matches the topology that this model actually contains.
Mediated Interface
Controlling Knobs
No direct knob in this model
Path toggles: c_rq*, coupled_window_length_m, PF branch lengths
Primary Matrix View
Use reduced Ydm,in(ω) for the qubit and S21 for the readout branch as a path-consistency check.
Expected Behavior
This effect must disappear if either the qubit↔resonator or resonator↔line interface is opened.
Changing PF geometry with c_rq = 0 should not move the qubit result.
The effect should look path-mediated, not like a brand-new direct capacitor.
If This Fails, Suspect
PF changes move the qubit even with c_rq opened.
The qubit responds as if there were a direct line coupling that is absent from the netlist.
Path-breaking toggles do not suppress the effect.
Actual behavior / plot slot
Insert: PF sweep with c_rq on/off, plus one path-break comparison panel.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
For mediated pairs, path-breaking null tests matter more than large parameter sweeps.

## Slide 13
13
Interface
Readout Resonator ↔ XY Line
Each pair should be audited by asking whether the parameter-response pattern matches the topology that this model actually contains.
Mediated Interface
Controlling Knobs
No direct knob in this model
Path toggles: c_rq*, c_xy*
Primary Matrix View
Use Ydm,in(ω) and selected full-matrix traces only as a mediated-effect null test.
Expected Behavior
This interaction should exist only through the shared qubit network.
Zeroing either c_rq or c_xy should kill the path.
Any residual feature should be small and systematic, not dominant.
If This Fails, Suspect
A strong RR↔XY effect remains after zeroing one side of the path.
A new standalone feature appears that cannot be routed through the qubit.
Trend magnitude is first-order when the topology only allows higher-order mediation.
Actual behavior / plot slot
Insert: c_xy / c_rq path-break matrix and one residual-effect summary.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
For mediated pairs, path-breaking null tests matter more than large parameter sweeps.

## Slide 14
14
Interface
XY Line ↔ Readout Line + Purcell Filter
Each pair should be audited by asking whether the parameter-response pattern matches the topology that this model actually contains.
Mediated Interface
Controlling Knobs
No direct knob in this model
Path toggles: c_xy*, c_rq*, coupled_window_length_m
Primary Matrix View
Use Ydm,in(ω) and branch S21 only as a mediated consistency check.
Expected Behavior
This is a second-order path through the qubit and resonator network.
Zeroing c_xy or c_rq should collapse the interaction.
Changing PF geometry alone should not change the XY-only reference case.
If This Fails, Suspect
PF geometry changes alter XY-only behavior without the readout path engaged.
The mediated effect is larger than the direct interfaces without a clear explanation.
Path-breaking toggles fail to suppress the effect.
Actual behavior / plot slot
Insert: XY-only versus XY+RO comparison with explicit path toggles.
Recommended inserts
One sweep plot with a monotonic knob on the x-axis
One null-test or decoupling-limit comparison
One sentence on whether the observed trend matches expectation
For mediated pairs, path-breaking null tests matter more than large parameter sweeps.

## Slide 15
15
Execution
How To Run The Audit
This last slide turns the deck into a repeatable protocol instead of a one-off presentation.
Per-Slide Fill-In Rule
Name the parameter being swept and which structure or interface it belongs to.
State the expected matrix signature before showing the plot.
Add the actual plot and one sentence: matched / partially matched / failed.
If it fails, point to the first plausible implementation surface to inspect.
Recommended Score Columns
structure_or_pair
swept_knob
primary_matrix_view
expected_trend
observed_trend
pass_status
confidence_delta
Minimum Black-Box Test Set
One monotonic self-sweep per structure
One zero-coupling or decoupling-limit test per direct interface
One path-breaking null test per mediated interface
One discretization or sweep-resolution refinement check on the final claim
One external-physics sanity check on magnitude or mode location
Decision Rule
Do not ask whether the implementation feels reasonable. Ask whether the necessary failure signatures stayed absent under the sweeps that should have exposed them first.
This protocol is designed for a researcher who cannot afford a full line-by-line code audit.